## Slide 1: Belo Matyko | July 2021
Locks Portfolio

## Slide 2: Product Categories
OEM Solutions
Locksets

## Slide 3: OEM Solutions
Lock Kits
MPL 415G
4-way-locks
Hardware
Lock cases
Other MPL

## Slide 4: Gear Locks (easy/smooth steering lock mechanism)
MPL415G
4-way-locks
cogwheel cylinder- cogwheel mechanism in the lock
cam cylinder- cogwheel mechanism in the lock

## Slide 5: 4-way-locks - 235,240,250,602
Use: Steel doors
Characteristics:
  Activated by cogwheel cylinder, Euro or Swiss profile
  Cogwheel mechanism- one turn
  10mm-13mm, Double D locking bolts, 20 mm bolt throw
  Fire rated
  En 12209 class 3-5 rated
  En 1627-1630 class 3 rated
  Need special hardware
  Accessories available

## Slide 6: Lock Kit for Multipoint Locks

## Slide 7: MPL 415G – Multipoint lock
Use: Steel doors
Characteristics:
  Double cylinder Lock
  Activated by cam cylinders, Euro profile
  Central Cogwheel mechanism- double turn
  Bolt throw 41 mm,
  3 bolts 18 mm Dia.
  Upper mechanism- double turn
  25 mm one bolt 18mm Dia
  Individual geometrical locking on each of the locking directions
  Lock kit available

## Slide 8: MPL 415G – multipoint lock set
Includes:
  Branded boxes
  Central lock
  Side locks- 2 pcs
  Adjustable bars for 1.92-2.12 door height
  Striking plates and screws
  Upper and lover striking boxes
  HS cylinder escutcheons - different finishes
  Cylinders – optionally!

## Slide 9
OTHER MULTIPOINT LOCKS

## Slide 10: Multipoint Lock 204A

## Slide 11: Multipoint Lock 352R
Category of use
Multipoint security lock for heavy duty steel doors.
Description
Activated by Euro cylinder with DIN cam mechanism.
Double Turn dead bolt function 17/35 mm
Features
LATCH-reversible (L,R option)
Suitable for auxiliary lock A103
Dimensions BS= 65, CC= 85, Bolts Diameter 16 mm X 3
Finishes
Front plate: Chrome-Nickel plated steel
Lock box: galvanized steel.
Bolts and Latch: Chrome-Nickel plated steel

## Slide 12: Multipoint Lock 104A
Category of use
Multipoint security lock for heavy duty steel doors-mounted during door assembling.
Description
Activated by Euro cylinder with DIN cam. Double rotation of the cylinder 29 (15+14) mm stroke.
Features
LATCH-reversible (L,R option)
When the bolts are in closed position the latch is disable with the handle.
Suitable for auxiliary lock A103
Dimensions BS= 65, CC1= 85, Bolts Diameter 18 mm
Finishes
Front plate: stainless steel
Lock box: galvanized steel.
Bolts and Latch: Chrome Nickel plated.

## Slide 13: Auxiliary lock A103
Suitable for general use as auxiliary lock.
352R
204A
104A
Double bolt with 18 mm diameter
FUNCTION:
BOLT STROKE 28mm
VERTICAL DROP 20+1.0 mm
LOCK FINISH:
Front plate: stainless steel
Lock box: galvanized steel.
Bolts and Latch: Chrome nickel plated.

## Slide 14
LOCK CASES

## Slide 15: Mortise Lock 354M
Category of use
Security lock for heavy duty steel doors.
Description
Activated by Euro cylinder with DIN cam. Double rotation of the cylinder 35 (17/18) mm stroke.
Features
LATCH-reversible (L,R option)
Handle spindle with ball bearing
Dimensions BS= 60, CC= 85, Bolts Diameter 16mm x 3
Finishes
Front plate: Chrome nickel plated
Lock box: galvanized steel.
Bolts and Latch: Chrome nickel plated.

## Slide 16: Mortise lock 277
Category of use
Security lock for all doors.
Description
Activated by Euro cylinder with DIN cam. Double rotation of the cylinder 20 (10/10) mm stroke.
Features
LATCH-reversible (L,R option)
Dimensions BS= 50, CC= 85, Bolts Diameter 12mm x 4
Finishes
Front plate: Satin Nickel plated
Lock box: galvanized steel.
Bolts and Latch: Satin Nickel plated .

## Slide 17: Mortise lock case 310-45A
Category of use
Security lock for all doors.
Description
Activated by Euro cylinder with DIN cam. Double rotation of the cylinder 20 (10/10) mm stroke.
Features
LATCH-reversible (L,R option)
Dimensions BS= 45, CC= 70, Bolts Diameter 14mm x 3
Finishes
Front plate: Chrome Nickel plated
Lock box: Black painted steel.
Bolts and Latch: Chrome Nickel plated .

## Slide 18: Lock 204S
Category of use
Security lock for all doors.
Description
Activated by Euro cylinder with DIN cam. Double rotation of the cylinder 20 (10/10) mm stroke.
Features
LATCH-reversible (L,R option)
Handle spindle with ball bearing
Dimensions BS= 45, CC= 85, Bolts Diameter 12mm x 3
Finishes
Front plate and Latch : Shine brass plated
Lock box: Black painted steel.
Bolts : Chrome Nickel plated .

## Slide 19: Lock 353P
Category of use
Auxiliary lock for steel doors.
Without latch and Handle
Description
Activated by Euro cylinder with DIN cam. Double rotation of the cylinder 35 (18/17) mm stroke.
Dimensions BS= 60, Bolts Diameter 16mm x 3
Finishes
Front plate: Chrome Nickel plated
Lock box: Black painted steel.
Bolts: Chrome Nickel plated .

## Slide 20: Lock 352K

## Slide 21: Lock 257 – Security Lever Lock
Category of use
Wood and steel doors
Characteristics:
  Preferred installation as additional lock for reinforcing security level.
  Deadlock mechanism- double turn
  Backset: 60 mm
  Triple round deadbolts: Ø16 mm
  Keyway protective plate hinders drill attacks
  Bolt throw = 18/35 mm
  Keys:3 or 5 double bit keys
  Cr/Ni plated front plate
  Galvanized steel box

## Slide 22
HARDWARE

## Slide 23: HARDWARE – SH 300
Use : 4-way Locks
Characteristics:
  Suitable for 4-way locks
  CC – 85 / 90 mm
  Friendly installation
  Moving handles and fixed handles versions
  Finishes: gold, nickel brushed and nickel satin

## Slide 24: HS Cylinder escutcheons for heavy duty locks
Use: compatible with all Euro profile cylinders and MTL multipoint locks
Characteristics:
  Hardened steel body
  Drill resistant rotating disk
  M8 screws
  Friendly installation
  Suitable for door thickness 50-75 mm
  Finishes: bright/satin chrome, bright brass, brushed nickel

## Slide 25
LOCKSETS

## Slide 26: HERCULAR Deadbolt
Use: High-security deadbolt system for commercial and residential doors.
Characteristics:
  Suitable for two backsets, no need for different parts
  Standards and drive-in
  Supplied as standard with 1” (25 mm) throw
  Optional as double or single cylinder
  Thumb turn tail self-adjustable to door thickness
  Option for captive key deadbolt
  Finish: US3, US26, US26D, US5A, US10B6
  UL Grade I rated

## Slide 27: CRONUS Deadbolt
Use: Provide protection for residential and commercial doors.
Characteristics:
  Suitable for two backsets, no need for different parts.
  High security KIK cylinder
  Robust cylinder protector
  Optional as double or single cylinder.
  Reinforced locking bolt
  Door thickness: 1⅜” (35 mm) to 1¾” (45 mm)
  Finish: PVD-Gold, polished stainless steel (US32), brushed stainless steel (US32D).
  UL Grade II rated

## Slide 28
DRAWINGS

## Slide 29: 4-way-locks - 235,240,250,602

## Slide 30: Mortise lock 277

## Slide 31: Mortise lock case 310-45A

## Slide 32: Lock 353P

## Slide 33: Lock 352K

## Slide 34: Lock 204S

## Slide 35: 204A

## Slide 36: A103

## Slide 37: 352R

## Slide 38: 354M

## Slide 39
Thank you